## Slide 1
How to Program a Drone to Fly with Python.

## Slide 2: Programming Background

## Slide 3
Did you know that instead of using a remote controller or mobile app, that you can write a computer program to fly a drone?

## Slide 4
Many electronic devices are controlled by computer programs (also called software).

## Slide 5
These devices use an Application Programming Interface or API to send commands to devices. An API translates computer programs into actions on a digital device. An API allows you to write computer programs for lots of different devices using the same programming language.

## Slide 6
If you know the Python Programming language, you can write programs for hundreds of different devices like those on the next page which all have Python APIs.

## Slide 7
Notes: https://micropython.org/
https://smartcar.com/docs/
https://github.com/dronekit/dronekit-python
https://github.com/NickWaterton/Roomba980-Python

## Slide 8
Pretend you are building a new drone that takes pictures of crops growing in fields. How could you make the drone fly the same route every day at the same time?
Notes: https://newsroom.statefarm.com/using-drone-technology-to-help-define-risk/

## Slide 9
API
Python Program
Device
“API, tell the drone to fly forward”
“OK, I’ll send your command to the drone”
“OK, API, I will fly forward”

## Slide 10
The Python programming language is one of the easiest, but also most powerful languages to learn.

## Slide 11: Programming the Drone

## Slide 12
So what does a real Python program look like?
On the next page, can you guess what these real Python commands are telling the drone to do?

## Slide 13
drone.takeoff()
drone.move_forward(50)
drone.rotate_counter_clockwise(90)
drone.flip(“f”)
drone.land()

## Slide 14
drone.move_forward(50)
This is the name of your drone in the program which is known as an “object”. We named the drone “drone”, but we can use any name.
The period separates our object from the command we want to send to the drone.
After the period, we have our command which is known as a “method” or “function”. This method tells the drone to fly forward.
Inside the parentheses, we are telling the drone how far forward to go. In this case, the “forward” method needs to know how far to go forward in centimeters. This is called a “argument” and can be any valid number for this method.

## Slide 15
drone.rotate_counter_clockwisew(90)
This is the name of your drone in the program which is known as an “object”. We named the drone “drone”, but we can use any name.
The period separates our object from the command we want to send to the drone.
This method tells the drone to rotate clockwise.
In this case, the method needs to know the number of degrees to rotate. You can use any number to tell the drone how much to rotate.

## Slide 16
drone.flip(“f”)
This is the name of your drone in the program which is known as an “object”. We named the drone “drone”, but we can use any name.
The period separates our object from the command we want to send to the drone.
This method tells the drone to flip.
Inside the parentheses, notice the “f” is inside quotation marks. Valid values here include the following:
“l” - left
“r” - right
“f” - forward
“b” - back

## Slide 17
drone.takeoff()
This is the name of your drone in the program which is known as an “object”. We named the drone “drone”, but we can use any name.
The period separates our object from the command we want to send to the drone.
This method tells the drone to takeoff and must be run before any other commands.
In this case, because there is only one way to takeoff, there are no arguments required within the parentheses.

## Slide 18
Python Command | English Translation
drone.takeoff() | Drone, takeoff.
drone.land() | Drone, land.
drone.move_up(25) | Drone, fly up 25 centimeters.
drone.move_down(25) | Drone, fly down 25 centimeters.
drone.move_left(25) | Drone, fly left 25 centimeters.
drone.move_right(25) | Drone, fly right 25 centimeters.
drone.move_forward(50) | Drone, fly forward 50 centimeters.
drone.move_back(50) | Drone, fly backward 50 centimeters.
drone.rotate_clockwise(90) | Drone, rotate in place 90 degree clockwise.
drone.rotate_counter_clockwise(90) | Drone, rotate in place 90 degree counterclockwise.
drone.flip(“f”) | Drone, do a forward flip. Valid params are “f”, “b”, “l” or “r”.

## Slide 19: Models and Simulations

## Slide 20
How do you think computer programmers test their programs for computer controlled machines like self-driving cars, rockets, and flying drones?
What happens when the computer program has mistakes in it?

## Slide 21
When mistakes in a computer program can cause a machine like a rocket or drone to crash, programmers often use a computer simulation to test the software before using it in the real world.

## Slide 22
Simulation Program
Program
Test Results
Real Rocket
Program
Rocket Flies or Crashes (Real Results)
Simulation
Production
Software
Software

## Slide 24
So, we are also going to use simulation to program our drone flights. This will allow us to test our program before we send it to a real drone.

## Slide 25
Once we open up Jupyter in our web browser, we can start writing our drone simulation program. The two commands shown below get us started.
This command loads our simulation software.
This command makes a Python object called “drone”.

## Slide 26
If our commands are run correctly, we should see the following output.

## Slide 27
What do you think our simulation will do if we make a mistake in our program? For example, what it we try to flip the drone before we take off?

## Slide 28
This is what an error looks like. We can see at the bottom, that the error tells us what we did wrong.

## Slide 29: Drone Program Commands

## Slide 30
drone.move_forward(50)
Lower case. No spaces.
Whole number without quotation marks.
Parentheses around parameter.

## Slide 31
drone.flip(“f”)
Lower case. No spaces.
Letter inside quotation marks.
Parentheses around parameter.

## Slide 32
drone .move_forward(50)
Extra space.

## Slide 33
Drone.Move_Forward(50)
Not lower case.

## Slide 34
drone.move_forward(“50”)
Quotation marks around number.

## Slide 35
drone.flip(f)
Letter parameter needs quotation marks.

## Slide 36
Now, let’s look at what the simulator does when we have a flight program with no errors. For this flight, we will:
Take off
Fly forward 50 centimeters
Turn right 90 degrees
Fly forward 100 centimeters
Land

## Slide 42: Sending Your Program to a Real Drone

## Slide 43
There are two different ways to send our program to a real drone to test it in the real world.

## Slide 44
Save our program and send it to someone else to run.
This can be any file name

## Slide 45
Connect to the Tello drone using your WiFi connection and send your program to the drone.

## Slide 46
You can get help in your Jupyter Notebook by running a command with a question mark after it.

## Slide 47: In-class Drone Exercise

## Slide 48
takeoff
STEP 1: Measure the drone course to build your flight program. Record the measurements to use when you are programming.
landing
1
2
3
4
5

## Slide 49
STEP 2: Create your programmed flight plan. Each line of your program is a different step for the drone.

## Slide 50: Run Your Simulation

## Slide 51
takeoff
STEP 3: The simulation will test your code and output a simulated path or model of your drone’s flight. If your program has no errors, when you run “all cells”, it will output plots of your flight path step by step.
50 cm
50 cm
150 cm
100 cm
landing
Simulated Path

## Slide 52
Did your program work as you expected?
Did the plots of the flight path match your plan?

## Slide 53: Test Your Model With a Real Drone

## Slide 54
takeoff
landing
STEP 4: Finally, you will deploy your programmed flight path to the drone and test it by connecting to the drone WiFi and deploying your code. The actual flight will likely differ from your model path.
50 cm
50 cm
150 cm
100 cm
Simulated Path
Actual Path

## Slide 55
Did the drone perform as expected?
Where did the actual flight differ from the simulated flight?
  What are some reasons for these differences?
If you flew your flight plan more than once, were there differences in the actual flight using the same program?
  Why might there be differences?
How could the simulation be made more accurate?
Could you adjust your program to make your actual flight better match your planned path?

## Slide 56: Models

## Slide 57
Can you think of any simulations or models that are used for natural phenomena?
  Why might such models be useful?
Can you think of any other simulations or models that are used for used for man-made or designed systems?
  Why might such models be useful?

## Slide 58
Word or Term | Definition
Computer Program | A computer program is a collection of instructions that performs a specific task when executed by a computer.
Computer Programming Language | A specific set of instructions that can be used to program a computer. This includes rules for what is correct and how to accomplish tasks.
Python | A computer programming language that is easy to learn, but also very powerful.
Computer Software | Computer software is a collection of instructions or programs that performs a specific task when executed by a computer.
API | A application programming interface is a program that translates instructions from a programming language to another system to make controlling a system easier.
Computer Simulation | A computer program that acts like a real device to test programs to see how they work in a safe environment.